## Slide 1: Machine Predictive Maintenance
November, 2022
Failure Classification

## Slide 2: Project objective: Deliver a product to Northrup Grumman to predict machine failure

## Slide 3: Data
Northrup Grumman
Notes: Where does the informatio come from?

## Slide 4: Data
Contains a data point for each product run through the machine
10000 points in dataset
Includes information on air temp, process temp, rotational speed, torque, tool wear, and failure
Northrup Grumman

## Slide 5: Range
Heat Dissipation, Power Failure, and Overstrain Failure are most common failures

## Slide 6: Relationships
Grouping between features show correlation between type of recorded data and type of failure

## Slide 7: Relationships
Notes: Torque, tool wear and rotational speed most important.
Want to avoid the following:
Torque (related to power failure): less than 20 Nm or more than 58 Nm
Tool Wear(related to tool wear failure): more than 190 minutes of use
Rotational speed (overstrain and heat dissipation failure): less than 1200 rpm

## Slide 8: RESULTS
Final Model predicted all values correctly except for 2 instances of power failure and 1 instance of tool wear failure as Overstrain failure

## Slide 9: FUTURE WORK
1. Expand Dataset
2. Alternative machines
Notes: Need to collect additional data on the current machine to test model performance more to ensure the model operates well
Will have to create new and different models for different machines as they are added

## Slide 10: CONCLUSIONS
Avoid the following to prevent failure:
  Torque (power failure): less than 20 Nm or more than 58 Nm
  Tool Wear (tool wear failure): more than 190 minutes of use
  Rotational speed (overstrain and heat dissipation failure): less than 1200 rpm
Final model 99% accurate with 97% precision

## Slide 11: THANK YOU